## Slide 1: How Manure Storage Impacts Farm Emissions

## Slide 2: OBJECTIVES
  Introduction to the emissions that come from manure
  Build awareness and understanding of some key manure emission mitigation options
  Debunk manure related myths
  There are many opportunities for GHG emissions reductions in manure management systems.

## Slide 3: AGENDA
Basics of Manure Emissions
Options to Reduce Manure Emissions
Debunking Manure Myths
Conclusion

## Slide 4: Basics of Manure Emissions

## Slide 5: MANURE EMISSIONS
Manure is often stored on dairy farms to recycle nutrients for crop production
Storage of manure generates greenhouse gases (GHGs)
Some factors that change the amount of emissions generated during storage:
  Temperature
  Time in storage
  Moisture content
  Composition of the manure

## Slide 6: GASES OF MANURE EMISSIONS
Methane (CH4)
Produced by bacteria breaking down manure in the absence of oxygen
Ammonia (NH3)
Produced from ammonium through microbial processes of nitrification (ammonium to nitrate) and de-nitrification (nitrate to nitrous oxide)
Nitrous Oxide (NO2)
Not a greenhouse gas, generated from the nitrogen in manure and urine

## Slide 7: Options to Reduce Manure Emissions

## Slide 8: NOT ONE SIZE FITS ALL
Manure handling is just one part of a dairy farm
Emissions come from many different sources within the farm system
There is no one size fits all when it comes to reducing emissions from manure, need to consider the housing type, farm goals, and emissions sources

## Slide 9: BIOGAS COLLECTION AND UTILIZATION
Microorganisms break down biodegradable material in the absence of oxygen
Anaerobic digestion creates biogas, a combination of methane, carbon dioxide, water vapor, and other gasses
Biogas can be combusted, used for electricity and heat, or even transformed into a natural gas replacement
Anaerobic Digestion
United States Environmental Protection Agency [EPA] 2024. AgSTAR: Practices to Reduce Methane Emissions from Livestock Manure Management. https://www.epa.gov/agstar/practices-reduce-methane-emissions-livestock-manure-management
Leytem, A.B., S. Archibeque, N.A. Cole, S. Gunter, A. Hristov, K. Johnson, E. Kebreab, R. Kohn, W. Liao, C. Toureene, and J. Tricarico. 2024. Quantifying greenhouse gas fluxes in agriculture and forestry: Methods for entity-scale inventory. Chapter 4: Quantifying greenhouse gas sources and sinks in animal production systems. https://www.usda.gov/oce/entity-scale-ghg-methods/download

## Slide 10
BIOGAS COLLECTION AND UTILIZATION
Covering manure storage with an impermeable cover, like plastic, allows for the capture of the gases produced
We can then combust the captured methane to convert it into carbon dioxide, a less detrimental greenhouse gas
Ammonia is still an air quality and emissions concern
Gas Capture and Flare
Methane is more than 28 times as potent as carbon dioxide at trapping heat in the atmosphere (EPA, 2023).
United States Environmental Protection Agency [EPA] 2023. Global Methane Initiative: The Importance of Methane. https://www.epa.gov/gmi/importance-methane,
United States Environmental Protection Agency [EPA] 2024. AgSTAR: Practices to Reduce Methane Emissions from Livestock Manure Management. https://www.epa.gov/agstar/practices-reduce-methane-emissions-livestock-manure-management

## Slide 11
MANURE STORAGE & MANAGEMENT
Acidification
Acidification refers to reducing the pH of manure by adding acid or other acidifying agents
Lowering pH can inhibit the activity of methanogens that produce methane
If the pH is low enough, ammonia emissions can be also be reduced
Sulfate can also help to control emissions
United States Environmental Protection Agency [EPA] 2024. AgSTAR: Practices to Reduce Methane Emissions from Livestock Manure Management. https://www.epa.gov/agstar/practices-reduce-methane-emissions-livestock-manure-management
Petersen, S., Andersen, A. and Eriksen, J. Effects of cattle slurry acidification on ammonia and methane evolution during storage. 2012. Journal of Environmental Quality 41:88–94. https://doi.org/10.2134/jeq2011.0184

## Slide 12
Gravity Systems
Separate waste with gravity (e.g., settling basin)
Can enhance GHG emissions depending on storage
Separating manure into liquid and solid portions can reduce the methane emission potential of liquid manure in storage, though some methods can instead enhance emissions. Separated solid matter can also be utilized in different ways (e.g., composting, recycled bedding, land-application) or stored.
Chemical Systems
These combine chemical methods like flocculation with mechanical systems
Can reduce GHG emissions
Mechanical Systems
Separate waste using machines (e.g., centrifugation)
Can reduce GHG emissions
The time that manure stays in the separation system may affect the overall reductions in methane.
SOLID LIQUID SEPARATION
United States Environmental Protection Agency [EPA] 2024. AgSTAR: Practices to Reduce Methane Emissions from Livestock Manure Management. https://www.epa.gov/agstar/practices-reduce-methane-emissions-livestock-manure-management
Leytem, A.B., S. Archibeque, N.A. Cole, S. Gunter, A. Hristov, K. Johnson, E. Kebreab, R. Kohn, W. Liao, C. Toureene, and J. Tricarico. 2024. Quantifying greenhouse gas fluxes in agriculture and forestry: Methods for entity-scale inventory. Chapter 4: Quantifying greenhouse gas sources and sinks in animal production systems. https://www.usda.gov/oce/entity-scale-ghg-methods/download

## Slide 13
Evaporation can be used to dry solids enough so that minimal or no microbial activity occurs while in (dry) storage
However, evaporating moisture takes energy!
Incorporating systems that serve as a heat source is ideal for reducing the amount of energy required
ADVANCED TREATMENT
Evaporation
United States Environmental Protection Agency [EPA] 2024. AgSTAR: Practices to Reduce Methane Emissions from Livestock Manure Management. https://www.epa.gov/agstar/practices-reduce-methane-emissions-livestock-manure-management
Leytem, A.B., S. Archibeque, N.A. Cole, S. Gunter, A. Hristov, K. Johnson, E. Kebreab, R. Kohn, W. Liao, C. Toureene, and J. Tricarico. 2024. Quantifying greenhouse gas fluxes in agriculture and forestry: Methods for entity-scale inventory. Chapter 4: Quantifying greenhouse gas sources and sinks in animal production systems. https://www.usda.gov/oce/entity-scale-ghg-methods/download

## Slide 14: ADVANCED TREATMENT
This process incorporates earthworms which stabilize carbon and nitrogen, move air and water through the manure, and produce worm castings (a value-added product).
Vermifiltration
Miito, G., Ndegwa, P., Alege, F., Coulibaly, S. 2022. Efficacy of a vermifilter at mitigating greenhouse gases and ammonia emissions from dairy wastewater. https://doi.org/10.1002/jeq2.20367

## Slide 15: COMPOSTING
Composting is the aerobic partial decomposition of manure organic matter
Emissions from composting vary by moisture content, temperature, carbon and nitrogen content, and the pH of the manure
Farms should consider the trade-offs between reducing
methane emissions vs. ammonia and nitrous oxide emissions.
United States Environmental Protection Agency [EPA] 2024. AgSTAR: Practices to Reduce Methane Emissions from Livestock Manure Management. https://www.epa.gov/agstar/practices-reduce-methane-emissions-livestock-manure-management
Leytem, A.B., S. Archibeque, N.A. Cole, S. Gunter, A. Hristov, K. Johnson, E. Kebreab, R. Kohn, W. Liao, C. Toureene, and J. Tricarico. 2024. Quantifying greenhouse gas fluxes in agriculture and forestry: Methods for entity-scale inventory. Chapter 4: Quantifying greenhouse gas sources and sinks in animal production systems. https://www.usda.gov/oce/entity-scale-ghg-methods/download
Notes: https://dairy.photoshelter.com/search/result/I0000B46yS66f92k?terms=compost&

## Slide 16: MANURE OPPORTUNITIES
Manure can produce:
  Energy through anaerobic digestion
  Livestock bedding
Biodegradable containers
Nutrient rich fertilizer
Lim, T., Massey, R., McCann, L., Canter, T., Omura, S., Willett, C., Roach, A., Key, N., and Dodson, L. 2023. Increasing the Value of Manure for Farmers. https://www.ers.usda.gov/publications/pub-details/?pubid=106088

## Slide 17: Debunking Manure Myths

## Slide 18: MANURE MYTH #1
One technology will enable me to achieve net zero
False! There is no one magic bullet to reduce emissions.
For example, installing a digester may help to reduce overall farm emissions but that only addresses one source of GHG on the farm, so just having a digester cannot get you to net zero GHG emissions!
Notes: https://dairy.photoshelter.com/galleries/C0000.P4WrHK5QIU/G0000RNaekCBZybg/I0000ht1IkHM.cNM/Jordan-Farm-1-jpg

## Slide 19: MANURE MYTH #2
A crust on liquid storage will decrease methane emissions.
Caution! In many cases, the crust does little to reduce methane emissions because it is not perfectly sealed and may not have uniform coverage. A crust can also generate other emissions like N2O, an important trade-off to consider!
Notes: https://dairy.photoshelter.com/galleries/C0000.P4WrHK5QIU/G0000RNaekCBZybg/I0000LJmY65exy70/MG-3031-jpg

## Slide 20: MANURE MYTH #3
Manure storage additives will reduce emissions.
Don’t believe everything you hear! Companies sell all sorts of additives and we often do not know if the products are viable or not.
Notes: https://dairy.photoshelter.com/galleries/C0000.P4WrHK5QIU/G0000RNaekCBZybg/I0000d7nSNgk46IU/HH-Pan-12-jpg

## Slide 21: Conclusion

## Slide 22: KEY TAKEAWAYS
Greenhouse gas emissions from stored manure contribute to the overall emissions footprint of dairy farms.
There are many available mitigation options, farms should determine the sources of manure emissions on their farms and consult experts to find the best strategies for their operations.
It is important to consider the entire manure management system and the goals of the farm when working to reduce emissions.
1
2
3